## Slide 1
MIT Academy of Engineering
SOFTY
Soft Touch Robotic Arm Gripper
Force-Sensing Based Adaptive Gripping System using ESP32
Ashutosh Sharma (202501070190) | Samrudhi Naik (202501070179) | Amruta Pawar (202501070177)
Guided by: Prof. Dhananjay Devare | Dept. of ENTC Engineering | May 2026
Course: Integrating Sensors & Actuators (2307162L)

## Slide 2
PRESENTATION OUTLINE
01
Introduction & Motivation
02
Problem Statement & Objectives
03
System Design & DAS
04
Components & Bill of Material
05
Simulation & Circuit Diagram
06
Observation Results & Graphs
07
Conclusion & Future Scope

## Slide 3
INTRODUCTION
Soft Robotics
Enables safe handling of delicate and fragile objects that conventional rigid grippers cannot manage.
The Problem
Conventional grippers apply fixed force with no feedback — causing object damage or insecure gripping.
Adaptive Sensing
Real-time force sensing is required to bridge the gap between rigid power and a delicate touch.
Our Approach
Integrating FSR-402 sensor + ESP32 + Servo for a closed-loop adaptive gripping system.

## Slide 4
PROBLEM STATEMENT & OBJECTIVES
Problem Statement
Conventional robotic grippers apply fixed force without sensing feedback, which can damage delicate objects or lead to inefficient gripping.
A system is required that can dynamically adjust grip strength based on real-time force feedback to prevent slippage or damage.
Objectives
Develop a soft-touch gripper featuring integrated force sensing capability.
Implement real-time, closed-loop control for precision gripping.
Ensure safe, adaptive gripping for delicate and fragile objects.
Monitor power consumption and implement overload protection.

## Slide 5
DATA ACQUISITION SYSTEM (DAS)
FSR 402
Sensor
Detects Grip
Pressure
ESP32
Micro controller
Processes &
Analyses Data
MG996R
Servo Motor
Adjusts Grip
Strength
Soft
Gripper
Precise Grip
Control
⟳ FEEDBACK LOOP — Continuous Monitoring & Adjustment
FSR sensor detects grip pressure → ESP32 processes analog signal → Servo adjusts position → Feedback loop maintains precise force.

## Slide 6
KEY COMPONENTS
ESP32 Microcontroller
3.3V • Wi-Fi 802.11 b/g/n
12-bit ADC • Dual-core
Multiple GPIO pins
MG996R Servo Motor (×2)
4.8V–7.2V • 9–11 kg·cm
PWM control • 0°–180°
High torque for linkage
FSR-402 Force Sensor
3.3V–5V via divider
Response < 10 ms
Analog output signal
Power Supply (5V, 2A)
5V DC stable output
≥2A current capacity
Prevents servo jitter
Resistors & Capacitor
10kΩ — voltage divider
2200µF — bulk decoupling
Signal conditioning
3D Printed Gripper
Soft silicone fingers
Linkage mechanism
Tapered finger design

## Slide 7
BILL OF MATERIALS
Component | Qty | Unit Cost (₹) | Total (₹)
ESP32 Development Board | 1 | 450 | 450
Servo Motor MG996R | 2 | 300 | 600
Force Sensitive Resistor FSR-402 | 1 | 250 | 250
Resistor 10kΩ | 2 | 5 | 10
Breadboard | 1 | 150 | 150
Jumper Wires | 20 | 2 | 40
External Power Supply (5V, 2A) | 1 | 200 | 200
Electrolytic Capacitor (2200µF) | 1 | 30 | 30
3D Printed / Mechanical Parts | 1 set | 300 | 300
Micro USB Cable | 1 | 150 | 150
TOTAL | 31 | — | ₹ 2180

## Slide 8
SIMULATION & CIRCUIT DESIGN
System Algorithm
1. Initialize ESP32, GPIO, Servo & FSR
2. Start Wi-Fi Access Point (AP mode)
3. Wait for User Command (Grab/Release)
4. READ FSR sensor value
5. IF force < threshold → close gripper
6. ELSE → stop servo, maintain grip
7. Monitor continuously
8. On Release command → open gripper
Simulation Verified on Wokwi
ESP32 + Servo + FSR Simulation
Potentiometer used as FSR-402 stand-in
Access Point Mode Verified
IP: 192.168.4.1 — Web server confirmed
Closed-loop control tested
Servo responds to FSR threshold changes
Simulation Links:
wokwi.com/projects/462837135965877249
wokwi.com/projects/460221539567272961

## Slide 9
OBSERVATION TABLE & RESULTS
FSR Value vs. Servo Angle
FSR Value (ADC) | Servo Angle | Gripper State
200 | 30° | Open
800 | 60° | Partially Closed
1500 | 90° | Holding
2500 | 110° | Firm Grip
Command vs. Response
Input Command | Servo Action | Result
Grab | Servo Closes | Object Gripped
Release | Servo Opens | Object Released
FSR Value vs. Servo Angle (Graph)
Chart: FSR Value (ADC)
| 0 | 250 | 500 | 1000 | 1500 | 2000 | 2500 | 3000
Servo Angle | 0 | 10 | 25 | 50 | 75 | 95 | 110 | 120

## Slide 10
CONCLUSION & FUTURE SCOPE
Conclusion
Successfully implemented a closed-loop, force-sensing gripper using ESP32 + MG996R Servo + FSR-402. The system dynamically adjusts grip strength in real-time via a wireless web interface, enabling safe and adaptive handling of delicate objects without damage. The design validates key embedded concepts: signal conditioning, PWM actuation, and real-time control.
Future Scope
Multi-DOF Arm
Extend to full 6-DOF robotic arm with object manipulation and positioning.
AI-Based Vision
Integrate camera + ML for autonomous object detection and adaptive grip.
Higher Precision Actuators
Replace servos with stepper or DC motors with encoders for finer control.
Industrial Applications
Scale to medical handling, food industry, and fragile object automation.

## Slide 11
Thank You!
Questions & Discussion
Project: Softy – Soft Touch Robotic Arm Gripper
Ashutosh Sharma • Samrudhi Naik• Amruta Pawar
MIT Academy of Engineering | ENTC Dept. | May 2026
Guided by: Prof. Dhananjay Devare
Video: youtu.be/d0LRWnBDcW4